## Slide 1: Sterilization
By Mamita Rai Gurung

## Slide 2: Sterilisation
Is defined as a process that completely destroys all types of microbial life including bacteria, their spores, viruses, fungi etc. Sterilisation can be done by physical, chemical, mechanical and radiation methods.

## Slide 3: Disinfection
Is defined as the reduction of the number of microorganisms or destroying pathogen on objects or in materials so that they pose no threats of disease and the object is said to be disinfected.If the disinfected object is nonliving the chemical used is called disinfectant.However is the object is living like tissue of the human the chemical used is called antiseptic.

## Slide 4: A. Physical methods of sterilization
    i. Sterilisation by high temperature:
Every organaism has its optimum, minimum and maximum growth temperature. Usually, temperature above maximum generally kills whereas below the minimum usually produces statis. Practical procedures by which heat is employed are divided as;
Dry heat (Flaming, incineration, Hotair oven)
Moist heat ( steaming below 1000c, steaming at 1000c, Inspissation, autoclave)

## Slide 5: a. Dry heat:
Generally used for materials like laboratory glass wares (petriplates, pipettes,oils etc)
Flamming: Flamming is just heating the material over Bunsen burner.Have the temperature of 1870oC. It is generally employed for sterilisation of inoculated loop or wire, mouth of flask etc.
Incineration: It is also simply destruction of microorganisms by burning. It is used for destruction of carcasses, infected laboratory animals, stool, contaminated dressing swabs and other materials that cannot be reused and should be disposed off. Precaution should be taken to ensure that exhaust fumes donot carry any particulate matter containing viable microorganisms into atmosphere.
Hot air oven: It is an electrically operated heating system used to sterilise laboratory glass wares, metal instruments, swab sticks etc. It contains fan to circulate hot air and a thermostst to maintain constant temperature. Usually hot air oven is operated at 160˚c for 60 minutes.

## Slide 6: b. Moist heat:
Moist heat method uses the combine effect of high temperature and high moisture and this method is more effective than the dry heat alone. Moist heat kills microorganisms by coagulating proteins.
Steaming below 100˚c: Pastuerization is usually done for sterilizing the milk .The milk is heated at 73ºc for 15-20 seconds or 63ºc for 30 minutes.
Boiling at 100˚c: steaming at 100ºc is usually done to sterilize some instruments, rubber tubings etc. Though it kills non sporing vegetative cells, some spores resist boiling for more than one hour.
Inspissation:This method is used to solidify protein media like Lowstein Jensen media using heat (75-80ºc) to coagulate. It is carried out either in an inspissator, oven or water bath.
Autoclave: It is a double jacketed steam chamber which is equipped with devices for desirable steam, temperature and pressure. Autoclave is commonly used in Microbiology laboratory to sterilize used conataminated culture media, solution, contaminated materials It is generally operated at 121ºc for 15lb/in2 and 15 mins.

## Slide 7: ii. Filtration:
Filters are used to stop bacteria. These special filters has known porosities usually ranging from 0.01-10µm. In laboratory, filters are used to sterilize heat sensitive substances such as serum, vaccines or for bacteriological water analysis process. Commonly used filters are;
Seitz filter (for sterilization of liquid media/ broth)
membrane filter ( for filtering water for bacteriological analysis)
High efficacy particulate air (HEPA) filter (used in laminar flow to produce dust/ bacteria free air)

## Slide 8: iii. Radiation
Different types of radiations are used for sterilisation purposes.
γ rays and X rays are ionisation raidations and such rays pass through cells and cause intracellular damage by creating free hydrogen radical, hydroxyl radical, peroxidases etc so called as ionizing radiation. Though this method is expensive and difficult to utilize, they have been used for experiments, research, commercial sterilization of packaged food, medical goods like vitamins,hormones etc.
UV light includes radiation from 100-400nm. Wavelength around 265nm has the highest bactericidal efficacy. Many lamps that emits UV lights are widely used to reduce microbial population extensively in hospital operating rooms, pharmaceutical industries etc. UV can damage nucleic acid of microorganisms forming pyrimidine dimers in which two adjacent pyrimidines becomes bonded. This bonding cause inhibition of DNA replication and mutation.

## Slide 9: B. Chemical methods of sterilisation
Chemical agents are effective by following mechanisms;
interfering with enzymatic system of organisms
disruption of cell membrane
coagulation of protein
oxidation

## Slide 10
The following chemicals are used as sterilizing agents;
Phenols: Phenols are used at a concentration of 2-5% to disinfect floors and materials such as sputum, urine, faeces, contaminated instruments etc. Phenols denature protein of cell membrane. Phenols are toxic to skin and tissues. Bacterial spores and viruses are more resistant to phenols than vegetative cells. Some of the common phenol derivatives are- Lysol, Cresol etc.
Alcohol: Ethanol and propanol (70% w/v) are generally used to reduce microbial flora of skin and for disinfection of oral thermometers. Alcohol denature the protein and lipid of cell membrane. Alcohols can be mixed with formalin or hypochlorite to improve its activity. However methyl alcohol is not used commonly because they are less bactericidal and more poisonous than ethyl alcohol.

## Slide 11
Aldehyde (RCHO):It inactivate proteins and nucleic acid. It is used in the form of formaldehyde or glutyraldehyde.
Formaldehyde:
In solution form, formaldehyde (formalin) is used to sterilize metal instruments like safety cabinets, hospital premises etc.
In gaseous form, it is used to sterilize heat sensitive catheters, fumigating wards, laboratories. The gas is irritant and toxic when inhaled.
Glutyraldehyde: It is the most effective chemical liquids for sterilization process.Destroy vegetative cells within 10-30 minutes and spore in 10 hrs.It is used in the concentration of 2% aqueous solution for sterilizing bronchoscope, surgical materials, anaesthetic tubes, centrifuge etc.

## Slide 12
Dyes and detergents: Dyes such as Aniline dyes and acridine dyes are generally used as antiseptiics on skin and wound. Dyes interfer with cell wall structure and DNA structure. Similarly detergents like soaps are used for cleansing purposes of skin, clothes etc and microorganisms are removed by rinsing. Detergents interfer the cell membrane structures.

## Slide 13
Heavy metals and their compounds:
Heavy metals interfer the microbial metabolism.
Common heavy metals and their compounds generally used are; Mercury (mercuric chloride, mercurous chloride, mercuric oxide), silver (silver nitrate), copper sulfate (copper sulfate).
Mercury compounds are toxic and corrosive so their use is limited though they are bactericidal.
Mercury chloride is generally used as antiseptic for treating skin disease.
Silver nitrate is used in eyedrops to prevent gonococcal infection of the eye.
Similarly, copper sulfate is used in swimminng pools and municipal water supply to control algae and molds.

## Slide 14
Halogens: Oxidise the protein. Commonly used halogens are iodine and chlorine.
Iodine in aqueous or alcoholic solutions is used to disinfect skin. It is used in several preparations like tincture of iodine, betadine etc.
Chlorine in liquid form is disinfection of drinking water and for disinfection of fomites. Generally chlorines are used in the form of bleaching powder, sodium hypochlorite or chloramine.
Gaseous agents: Commonly used gases are ethylene oxide, formaldehyde and β-propiolactone. Ethylene oxide is used to sterilize syringes, dental equipments and other plastic materials. Formaldehyde (gaseous) and β-propiolactone are mostly used for fumigation of rooms.

## Slide 15: An ideal antiseptic or disinfectant should have following properties
Wide spectrum of activity
Active in the presence of organic matter.
Effective in acidic and/or alkaline media
Speedy action
High penetrating power
Stable
Not corrosive
Not causing local irritation or sensitization
Not interfering with healing
Not toxic if absorbed into the cirrculation
Cheap and easily available.

## Slide 16: Some common terms
Antiseptic: a substance that opposes sepsis i.e prevents the growth or action of microorganisms on the living tissue either by destroying microorganisms or by inhibiting their growth and metabolism Antiseptics is usually associated with substances applied to the body.
Bactericide: An agent that kills bacteria. Similarly the terms fungicide, viricide and sporicide refers to the agents that kills fungi, viruses and spores respectively.
Bacteriostatic: It is a condition in which the growth of bacteria is prevented by preventing the multiplication of micro organisms without necessarily killing them.
Antimicrobial agent: Agents that interferres with the growth and metabolism of microbes, Antimicrobials against bacteria are called antibacterial agents and agents used to treat infections are called chemotherapeutics agents.